## Slide 1: Short message service (SMS)

## Slide 2: Index
Introduction
Explanation and uses of SMS
Application of SMS

## Slide 3: introduction
SMS stands for short message service. It is a technology that enables the sending and receiving of messages between mobile phones.
SMS first appeared in Europe in 1992. It was included in the GSM (global system for mobile communications) standards right at the beginning.
Later it was ported to wireless technologies like cdma and tdma. The GSM and SMS standards were originally developed by ETSI. ETSI is the abbreviation for European telecommunications standards institute.
Now the 3gpp (third generation partnership project) is responsible for the development and maintenance of the gsm and sms standards.

## Slide 4
one drawback of the sms technology is that one sms message can only carry a very limited amount of data.
overcome this drawback, an extension called concatenated sms (also known as long sms) was developed.
a concatenated sms text message can contain more than 160 english characters.
concatenated sms works like this: the sender's mobile phone breaks down a long message into smaller parts and sends each of them as a single sms message.
when these sms messages reach the destination, the recipient mobile phone will combine them back to one long message.
the drawback of concatenated sms is that it is less widely supported than sms on wireless devices.

## Slide 5: explanation
An SMS center (SMSC) is responsible for handling the SMS operations of a wireless network. When an SMS message is sent from a mobile phone, it will reach an SMS center first.
The sms center then forwards the sms message towards the destination. An SMS message may need to pass through more than one network entity (e.g. SMSC and SMS gateway) before reaching the destination.
The main duty of an smsc is to route sms messages and regulate the process. If the recipient is unavailable (for example, when the mobile phone is switched off), the SMSC will store the SMS message. It will forward the SMS message when the recipient is available.

## Slide 6
Very often an SMSC is dedicated to handle the SMS traffic of one wireless network.
A network operator usually manages its own smsc(s) and locates them inside its wireless network system.
However, it is possible for a network operator to use a third-party smsc that is located outside the wireless network system.
You must know the address of the wireless network operator's smsc in order to use sms messaging with your mobile phone.
Typically an smsc address is an ordinary phone number in the international format.

## Slide 7: Uses of SMS
Text messages are short, quick, and very personal.
Consumers who invite marketers into the walled garden of sms do so much more selectively than any other channel.
As a result, senders who fail to deliver relevant, useful text messages are quickly greeted with a “stop” reply.
The sms channel is particularly adept at delivering alert messaging.
In fact, this is the one type of messaging that indexed high enough to be considered appropriate by a majority of consumers.
That’s not to say, however, that you can simply assume that consumers who provide their mobile numbers want to receive text messages from you.

## Slide 8: strengths
Alerts
Event interactions
Event messaging
In-store promotions
Mobile marketing opt-ins
Personal interaction
Emergency notification
Reminders

## Slide 9: applications
SMS as an appointment reminder.
Sms as a planning tool.
Sms as an internal communication and notification tool.
Sms as an external marketing channel.
Sms for server notifications.
Sms as your login code.
Sms for voting.
Sms for applications and requests.

## Slide 10: conclusion
while many SMS applications for disease prevention exist, few have been evaluated. The dearth of peer-reviewed studies and the limited evidence found in this systematic review highlight the need for high-quality efficacy studies examining behavioral, social, and economic outcomes of SMS applications and mobile phone interventions.

## Slide 11: Thank you